## Slide 1: 13. Mobile Device Forensics - Part 1

## Slide 2: Topics
Cellular Networks
Cell Phone Operating Systems
Evidence on Cell Phones

## Slide 3: Cellular Networks

## Slide 4: Cell Phone Basics
Important evidence
  Emails & SMS messages
  Internet history
  GPS (Global Positioning System)
  Photos
  Videos
Challenge: Diversity
  Many makes, models, and operating systems
  No standard hardware interface
  More of them now have mini USB or micro USV

## Slide 5: Cell Phone Tower
Also called “Base Transceiver Station” or “Cell Site”
Image from Wikipedia (Link 10a)

## Slide 6: Cell Network Components
Base Station
  Antennas and related equipment
Base Station Controller (BSC)
  Regulates the signals between base stations
  Critical as phones move from place to place
Mobile Switching Center (MSC)
  Processes calls within the network
  Holds a lot of evidence
  Coordinates calls between different wireless networks and land lines
  Handles SMS messages
  Call detail records and logs are here

## Slide 7: Cell Network Components
Visitor Location Register (VLR)
  Database linked to a MSC
  All mobile devices currently being controlled by that MSC are recorded in the VLR
  Interworking functions are gateways to outside data networks such as the Internet
Home Location Register (HLR)
  Information about individual subscribers
  ID, billing, and services
  Stores encryption keys
  Supports Authentication Center (AuC) which controls access to the network

## Slide 8: Cell Network Components
Short Message Service Center (SMSC)
  Responsible for SMS messages
  Messages may be recovered
  No rule dictating how long providers must keep those messages

## Slide 9: Handoff
Each cell phone is regularly communicating with nearest cell tower
Even if it’s not in use
It sends identification data to the tower
  Cell phone number and service provider
Handoff is the transfer from tower to tower as you move

## Slide 10: Handoff
Handled differently in GSM & CDMA networks
  GSM (Global System for Mobile Communication)
    Hard handoff: Phone can only attach to one tower at a time
  CDMA (Code Division Multiple Access)
    Soft handoff
    Phone can connect to multiple towers at once
Records showing when a phone was connected to a tower can determine the approximate location of that phone

## Slide 11: Mobile Switching Center (MSC)
Once your call hits the tower it’s transferred to the MSC
If you are calling a phone outside the network, call is passed to the PSTN (Public Switched Telephone Network)

## Slide 12: Messaging Services
SMS (Short Message Service)
  Text messages
  Maximum of 160 characters
MMS (Multimedia Messaging Service)
  Improved functionality
  No 160 character limit

## Slide 13: Types of Cellular Networks
CDMA (Code Division Multiple Access)
GSM (Global System for Mobile Communications)
iDEN (Integrated Digitally Enhanced Network)

## Slide 14: CDMA (Code Division Multiple Access)
Originally military technology
Uses spread spectrum
Used by Sprint, Verizon, Alltel, and NEXTEL
Does not use SIM (Subscriber Identity Module) cards
Handsets identified by Electronic Serial Number (ESN)
  ESNs have 32 bits and ran out in 2010, and the new system, MEID, has replaced it
  MEID has 56 bits (Link Ch 10b)

## Slide 15: GSM (Global System for Mobile Communications)
Used internationally
Uses Time Division Multiple Access (TDMA)
Uses SIM (Subscriber Identity Module) cards
Carriers include AT&T, Verizon, T-Mobile and Cellular One
Handsets identified by International Mobile Equipment Identity (IMEI) numbers (15 or 16 digits)

## Slide 16: IMEI Blacklist
IMEI uniquely identifies phone, and is not changed by replacing the SIM card
IMEI can be used to blacklist stolen phones
  Links Ch 10c & 10d

## Slide 17: iDEN (Integrated Digitally Enhanced Network)
Two-way radio-like functionality
Supports normal phone users and “push-to-talk” dispatch users
Sprint will stop supporting iDEN in June, 2013
  Link Ch 10e

## Slide 18: Prepaid Cell Phones
Can be purchased with cash
No trail to the identity of the user
Cell phone will hold any subscriber information
Network provider will have call details
  Location and calls sent and received

## Slide 19: Cell Phone Operating Systems

## Slide 20: Modern Cell Phone Operating Systems
Symbian
Apple iOS
Windows CE and Windows Mobile
Google’s Android
Blackberry OS

## Slide 21
Link Ch 10f

## Slide 22: Symbian
Started as EPOC in the 1980s
First used on phones in 2000 by Sony
Passed through many different companies
Nokia recently made it open-source
In 2011, Nokia switched to Windows Phone
Accenture continues to support Symbian

## Slide 23: Blackberry
Introduced in 1999 by Research In Motion (RIM) from Canada
Common at workplaces
Synchronize with Novell’s GroupWise and Microsoft’s Exchange
Different OS versions for each carrier

## Slide 24
Link Ch 10h

## Slide 25: Android
The most popular OS by far
Open Source
Used on Motorola, Sony Ericsson, and HTC phones
Also on tablets

## Slide 26: Apple’s iOS
Used on iPhone, iPad, and iPod Touch
Based on OS X
Second most popular phone OS

## Slide 27: Windows Mobile (now Windows Phone)
Windows OS versions for smartphones and pocket PCs
Windows Phone 8 was released in Oct. 2012
  Link Ch 10i

## Slide 28: Evidence on Cell Phones

## Slide 29: Potential Evidence Items
Call history
Text messages (active & deleted)
Email
Photos & video
Browser history
Contacts
GPS location information
Chat sessions
Calendar
Voice memos
Documents

## Slide 30: PIN (Personal Identification Number)
Can be used to secure the handset
Three failed attempts will lock the SIM
A Personal Unlock Key (PUK) is needed to unlock the SIM
  PUK comes from the provider of the SIM card
Image from link Ch 10j

## Slide 31: Predictive Text
Intended to make it easier to type on 10-digit keypads
Fills in text when the user types part of a word
  System learns frequently used words
  Database may contain words, slang, abbreviations, E-mail addresses or URLs
Also creates hilariously mangled messages
  Link Ch 10k

## Slide 32: Call Detail Records (CDR)
Used by the provider to troubleshoot and improve performance
May show:
  Date/time call started and ended
  Who called who
  Whether call was incoming or outgoing
  Originating and terminating towers
But you can’t tell who was holding the phone
Subscriber information is different from CDR
  Name, address, acct. numbers, email address, credit card #

## Slide 33: Retention Policies
Link Ch 10l

## Slide 34
Software included in phones to send tracking data back to the carrier
Privacy controversy (Link Ch 10m)

## Slide 35: Locating Cell Phones
Triangulation
  Measure signal delay to three nearest towers
  Can give approximate location of phone
Directional antenna
  Enables location determination with only two towers from delay measurements
GPS
  Locates cell phone with satellites
Wi-Fi Positioning System
  Uses data on known Wi-Fi access points
  Included on the iPad
  Link Ch 10n

## Slide 38
Triangulation images from link Ch 10o